Q4 (20 points) Answer the following:
a. (5 points) What decimal number does the bit pattern 0×0C000000 represent if it is a two’s complement integer? An unsigned integer?
Binary:0000 1100 0000 0000 0000 0000 0000 0000
Two's Complement: you can tell that the number is positive so it is the same as unsigned integer
both are 201,326,592

b. (5 points) If the bit pattern 0×0C000000 is placed into the Instruction Register, what MIPS instruction will be executed?
This would be a jump and link to the address 0

c. (10 points) What decimal number does the bit pattern 0×0C000000 represent if it is a floating point number? Use the IEEE 754 standard.
Binary:0000 1100 0000 0000 0000 0000 0000 0000
sign: 0 exponent:0b00011000-127=-103 fraction=1+000 0000 0000 0000 0000 0000
so Floating Point number = 1*2^-103 or (I used a calculator for this part) 9.860761e-32

Q5 (30 points) Answer the following
a. (10 points) Write down the binary representation of the decimal number 63.25 assuming the IEEE 754 single precision format.
63.25=0b111111.012=1.11111012*2^5 exponent =5+127=100001002
so single precision is 0-1000 0100-111 1101 0000 0000 0000 0000(dashes added for ease of grading)

b. (10 points) Write down the binary representation of the decimal number 63.25 assuming the IEEE 754 double precision format.
Exponent=1023+5 fraction stays the same with more zeros after
0-100 0000 0100-1111 1010 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000

c. (10 points) Write down the binary representation of the decimal number 63.25 assuming it was stored using the single precision IBM format (base 16, instead of base 2, with 7 bits of exponent).